## Slide 1: Homemade Hardware Keylogger/PHUKD Hybrid
Adrian Crenshaw

## Slide 2: About Adrian
I run Irongeek.com
I have an interest in InfoSec education
I don’t know everything - I’m just a geek with time on my hands
I’m an (Ir)regular on the InfoSec Daily Podcast: http://isdpodcast.com
Co-Founder of Derbycon http://www.derbycon.com/
Twitter: @Irongeek_ADC
Notes: Take a note from Johnny Long’s book, and Bruce Potter’s book.

## Slide 3: Hardware keyloggers
Hardware keyloggers are fairly simple devices conceptually
Essentially they are installed between the keyboard and the computer, and then log all of the keystrokes that they intercept to their onboard flash memory
A snooper can then come along later to pick up the key logger and extract the captured data (passwords, documents, activity, etc.)

## Slide 4: How this all started
Irongeek, the quest for free stuff!!!
Web traffic = toys!!!

## Slide 5: What is a Hardware Key Logger?
Pics http://www.keelog.com/ and http://www.keycarbon.com
Internal
External

## Slide 6: Advertised Uses (Come on vendors, admit it)
Writers: Users can install them on their own systems as a backup for the work they've typed in. :S
Businesses: Some companies may use keyloggers for monitoring employees for misconduct. :S
Parents: Some parents may choose to use a hardware keylogger to monitor their kids. :S
Pen-testers/Crackers/Spies/Jealous Significant Others: If an attacker is trying to get someone else's password or proprietary information hardware keyloggers can come in quite handy. :)
Legal?

## Slide 7: Cons
Harder to recover keystrokes remotely There's no chance of emailing or grabbing the keystroke logs from over a network; the device has to be physically recovered to obtain the logs. (well, there are a few little exceptions of sorts, Bluetooth, some TEMPEST/Van Eck phreaking, 27MHz interception, and maybe Seeing using the “licensing dongle” scheme)
Less information The hardware keylogger gives little to no information on what app was active when the keystrokes happened.
$$$$ Hardware keyloggers are rather expensive.
Easy to remove, if found If found, external hardware keyloggers are much easier to remove than software keyloggers. You just pluck them off the keyboard's cord. Removing software keyloggers depends on the user’s privilege level, or how knowledgeable they are about how to gain a higher privilege level. ☺

## Slide 8: Pros
Stealth Most software keyloggers are detected by anti-malware apps. Depending on which software package is used, the anti-virus system will likely detect the keylogger and remove it, or at the very least report it to the user. Hardware keyloggers, on the other hand, are very hard to detect without physical inspection. That's not to say it's impossible.
All keystrokes, independent of boot state Hardware keystroke loggers can get keystrokes from before the OS is even loaded (hello bios password), or from around software that limits what processes can access the keystrokes (like the Windows GINA logon after the old three finger salute of Ctrl-Alt-Del).
OS Independent Hardware keyloggers can support logging of almost any OS, as long as the keyboard is a fairly standard USB HID (Human Interface Device). Windows, Linux, Mac OS X - it makes little difference to a hardware keylogger.

## Slide 9: Models
Got mine awhile back, so I’m trying to match up prices with current offerings.
Name | Keys | Type | Price (may not be accurate) | Picture
KeyCarbon | Type: phxlog | Virtual keyboard and rapid downloader software | $147 - $297 | 
KeyGhost Plug | Type: vghostlog | Virtual keyboard | $249 | 
KeyGhost Cable | Type: vghostlog | Virtual keyboard | $349 | 
KeeLog | Hold down: k+b+s | Flash Drive | $44.99 | 
KeeLogUSB (KeyLlama rebrand) | Hold down: k+b+s | Flash Drive | $44.99 | 
KeeLogPS/2 (KeyLlama rebrand) | Hold down: k+b+d | Virtual keyboard and Flash Drive with adapter | $38.99 | 

## Slide 10: Detection and Mitigation
Physical security
Lockdown what hardware can be installed may work in some cases but not many
Physical inspection
Notice odd problems that could mean there is a USB keylogger present
  Odd USB vendor/product IDs?
  Inline devices not working from a keyboard’s built-in hub?
  Reports of slow USB speed with inline devices?

## Slide 11: How about making your own?

## Slide 12: Objective: Combining Keyloggers and Programmable HIDs
Log all the keys using a MicroSD card
Vary payloads based on keystrokes
Log username/password and use them later
Screw with the person who is typing
Flexible hobbyist platform to add new functionality
  WiFi
  Bluetooth
  Ethernet

## Slide 13: Programmable HID
Pre-Program Keystrokes
Auto-run being disabled does not matter
Cheap ($16 Teensy)
Payloads:
Add a user
Run a program
Copy files to your thumb drive for later retrieval
Upload local files
Download and install apps
Go to a website they have a cookie/session for, and do a sort of CSRF (sic)

## Slide 14: Setup Development Environment
Get the following files and install in this order (I assume you already have a working Java RE)
  Arduino Dev Package http://arduino.cc/en/Main/Software
  Teensyduino and the serial drivers http://www.pjrc.com/teensy/td_download.html
  Teensy Loader http://www.pjrc.com/teensy/loader.html
  PHUKD Library http://www.irongeek.com/i.php?page=security/programmable-hid-usb-keystroke-dongle
Put the Phuked folder in the \arduino-1.0\libraries directory
Set the board type

## Slide 15: Parts
Teensy ($16) http://pjrc.com/store/teensy.html
PS/2 Female Cable (Free?) (Cut it off a KVM cable or something)
SD Adapter ($8) http://pjrc.com/store/sd_adaptor.html
USB Host Adapter ($14.90) http://www.sure-electronics.com/goods.php?id=1140

## Slide 16: Libraries
PHUKD Library http://www.irongeek.com/i.php?page=security/programmable-hid-usb-keystroke-dongle#Programming_examples_and_my_PHUKD_library
Teensy PS/2 Library (I have my own mod of this which comes with the PS/2 Key Logger source code) http://www.pjrc.com/teensy/td_libs_PS2Keyboard.html
SDFat16Lib (I used the Wrapper that comes with Arduino) http://code.google.com/p/sdfatlib/

## Slide 17: PS/2 Keylogger
Going old school!

## Slide 18: PS/2 Scan Codes
Scan Codes read from the PS/2 Connection
Defined in the Teensy PS/2 Library with #Defines and Arrays
Have to translate to USB, which makes things tougher
Key | Code | Release
A | 1C | F0, 1C
B | 32 | F0, 32
C | 21 | F0, 21
D | 23 | F0, 23
E | 24 | F0, 24
F | 2B | F0, 2B
G | 34 | F0, 34

## Slide 19: PS/2 Keylogger
Pin 1 | +DATA | Data
Pin 2 | Not connected | Not connected*
Pin 3 | GND | Ground
Pin 4 | VCC | +5 V DC at 275 mA
Pin 5 | +CLK | Clock
Pin 6 | Not connected | Not connected**
Info and PS/2 pic from Wikipedia
+CLK/IRQ
+DATA

## Slide 20: PS/2 Keylogger Code and Demo

## Slide 21: USB Keylogger
User Recording Programmable HID USB Keyboard Dongle
=
UR PHUKD

## Slide 22: Programming: What you will need
We will need something to program it with
PICKit 2 Programmer (clone) http://www.sureelectronics.net/goods.php?id=21
PICkit 2 Development Programmer/Debugger Official Software http://www.microchip.com/stellent/idcplg?IdcService=SS_GET_PAGE&nodeId=1406&dDocName=en023805
MPLAB IDE X Beta 7.02MPLAB C30 Lite Compiler for dsPIC DSCs and PIC24 MCUs (Use lite options) http://www.microchip.com/en_us/family/mplabx/index.html

## Slide 23: USB Keylogger
RX on USB Module to TX on Teensy
TX on USB Module to RX on Teensy

## Slide 24: Getting the source…
Had to get Sure Electronics to send me the source
Took some convincing
Your mostly on your own for support
Code and HEX files http://www.sure-electronics.net/download/index.php?name=MB-CM13111&type=0
HID: Raw Report 00-00-13-00-00-00-00-00-
p
HID: Raw Report 00-00-13-00-00-00-00-00-
p
HID: Raw Report 00-00-13-00-00-00-00-00-
p
HID: Raw Report 00-00-13-00-00-00-00-00-
p

## Slide 25: USB To Serial To USB
HID Keyboard Reports
Key(s) | Code
a | 0000040000000000
Left Ctrl+Shift+Alt | 0700000000000000
Right Ctrl+Shift+Alt | 7000000000000000
a+b+c | 0000050406000000

## Slide 26: USB Keylogger Code and Demo

## Slide 27: More Ideas
Arduino community supports so many peripherals, what might be possible?
Wireless keylogger?
Ethernet keylogger?
Time Stamping
Make the key loggers more passive.

## Slide 28: Conclusions/Problems solved
Homemade Key Logger worked
Integrated with Programmable HID
Kept the costs low PS/2 unit = $24 and USB unit = $39 (Depending)

## Slide 29: Current Problems
Not passive
If the keyboard has a USB hub in it, it won’t work with the USB host module I currently use
Kind of hard to package it smaller

## Slide 30: Way more links than you ever wanted
AKA: Homework

## Slide 31: Useful Tools/Links
Homemade Keylogger/PHUKD Hybrid http://www.irongeek.com/i.php?page=security/homemade-hardware-keylogger-phukd
PHUKD Project site http://www.irongeek.com/i.php?page=security/programmable-hid-usb-keystroke-dongle
Paul’s Teensyduino Docs http://www.pjrc.com/teensy/teensyduino.html
USBDeview http://www.nirsoft.net/utils/usb_devices_view.html
Reg From App http://www.nirsoft.net/utils/reg_file_from_application.html
HAK5’s Rubber Ducky Forum http://www.hak5.org/forums/index.php?showforum=56

## Slide 32: Sources for more parts
Teensy http://www.pjrc.com/teensy/
Sure Electronics http://www.sure-electronics.com/
Ebay http://www.ebay.com/
Photoresistors and other small parts http://www.bgmicro.com http://www.mouser.com
LEDs http://www.ledshoppe.com/
Other stuff Small USB A to Mini USB http://www.dealextreme.com/details.dx/sku.2704~r.48687660 Small HUB http://www.dealextreme.com/details.dx/sku.30564~r.48687660

## Slide 33: Keylogger Links
Hardware Keyloggers: Use, Review, and Stealth (Phreaknic 12) http://www.irongeek.com/i.php?page=videos/pn12/irongeek-hardware-keyloggers-use-review-and-stealth
Hardware Key Logging Part 1: An Overview Of USB Hardware Keyloggers, And A Review Of The KeyCarbon USB Home Mini http://www.irongeek.com/i.php?page=security/usb-hardware-keyloggers-1-keycarbon
Hardware Key Logging Part 2:A Review Of Products From KeeLog and KeyGhost http://www.irongeek.com/i.php?page=security/usb-hardware-keyloggers-2-keyghost-keelog
Hardware Key Logging Part 3: A Review Of The KeyLlama USB and PS/2 Keyloggers http://www.irongeek.com/i.php?page=security/ps2-and-usb-hardware-keyloggers-3-keyllama
Hardware Keyloggers In Action 1: The KeyLlama 2MB PS/2 Keylogger http://www.irongeek.com/i.php?page=videos/keyllama-ps2-keylogger
Hardware Keyloggers In Action 2: The KeyLlama 2GB USB Keylogger http://www.irongeek.com/i.php?page=videos/keyllama-USB-keylogger

## Slide 34: Malicious USB Links
Plug and Prey: Malicious USB Devices http://www.irongeek.com/i.php?page=security/plug-and-prey-malicious-usb-devices
Malicious USB Devices: Is that an attack vector in your pocket or are you just happy to see me? http://www.irongeek.com/i.php?page=videos/malicious-usb-devices-phreaknic-14

## Slide 35: Events
Derbycon Sept 27th-30th 2012 http://www.derbycon.com
Others
http://www.louisvilleinfosec.com http://skydogcon.com http://hack3rcon.org
http://phreaknic.info http://notacon.org http://outerz0ne.org
Photo Credits to KC (devauto)
Derbycon Art Credits to DigiP
Notes: Beg for hardware donations. 

## Slide 36: Questions?
42
Twitter: @Irongeek_ADC